## Slide 1: Binary Logic Brief History
  In 1945 John von Neumann published a document that identified the principles behind the modern computer:
    Both data and programs are stored in the same place in the computer’s memory
    Both data and instructions are stored in binary
  Binary is a number system using only 0 and 1 to represent all numbers.
  Computers use binary because 1 and 0 can be represented very easily using simple electronic components set into the ON or OFF state (a switch).

## Slide 2: Binary Logic
The digital computer uses an arrangement of tiny electronic switches (transistors) called logic gates connected together.
These logic gates are used to manipulate the signals within the processor.
The arrangement of the switches in the logic gate determines what it does to the input signal.
The logic gates are all connected to allow the processor to receive and pass on electronic signals

## Slide 3: Binary Logic
  The circuit to store a single bit of data is made from a transistor and a capacitor.
  A capacitor can store electrons, and it can be in one of two states:
    ‘charged’, full of electrons;
    ‘discharged’, empty.
  A transistor is a switch that allows the control circuit to:
    check if there is a charge stored in the capacitor or not;
    change the state of the capacitor.

## Slide 4: Binary 1 or 0
Computer ONLY understand binary. A binary digit can only be either 1 or 0.
By arranging 1’s and 0’s together in special ways we can create anything!
  Numbers
  Letters
  Pictures
  Music
  Software!
When you read text on a screen the computer sees a series of 1’s and 0’s!

## Slide 5: Why is Data Represented in Computer Systems in Binary Form?
The denary (decimal) system that we use has 10 digits (0-9).
For a computer systems to use denary it would need to be able to store and transmit 10 different ‘states’.
It is therefore much simpler for computer systems to use the binary number system because it has just 2 digits (0-1) which can easily be represented and stored as 2 different states.
Examples of different ‘states’ used to store/transmit binary data:
  ON / OFF (a semi-conductor switch, used in computer memory)
  TRANSMIT / DON’T TRANSMIT (an electrical signal, used to transfer binary data)
  NORTH / SOUTH (areas with different magnetic polarity, used to store binary data on magnetic media)
  REFLECT / NON-REFLECT (reflective and non-reflective areas, used to store binary data on optical media)

## Slide 6: Implications of Binary
Ever wondered why computer memory has odd sizes? Like 256 Mb or 512 Mb or 1024 Mb?
We already know computers use binary...
This means we use binary or “base 2” for sizes.
ALL sizes on computers are 2x So……
the pattern will be 2, 4, 8, 16, 32, 64, 128, 256, 512, 1024, 2048 and so on.

## Slide 7: Activity
Add a new section to your revision notes called binary logic. Explain
What is binary?
Why do computers use binary?

## Slide 8: Answers
What is a binary
Binary is a base 2 8-bit number system represented by the numeric values of 0 or 1, also known as OFF or ON, and is the primary language that computers use to communicate.
Why do computer use binary?
Computers use binary because;
It is the easiest and most efficient method of detecting an electrical signal as being either off or on,
It is the most efficient way of detecting magnetic poles with magnetic media like a hard drive, and
It is the most efficient way to control logic circuits.

## Slide 9: What is Binary Logic
Computers use binary logic to do many great things.
It is one of the key skills needed in order to be able to program a computer.
It also helps to understand why computers can be a “bit thick” sometimes. More on that later 
Binary logic is where we say if something is either true or false. There is no maybes or kind of. Just true or false.
For example “Is that a car?” would result in true or false.
Or “Mr Jalloh has a beard today”.
Statements like “Is Mr Jalloh is awesome?” would NOT be binary logic as the answer will not be answered the same by different people.

## Slide 10: Predictable
Binary logic must be predictable.
That means that if you asked anyone you would always get the same true or false answer.
We must be able to predict the outcome.
The posh name for Binary logic is deterministic.
You do not need to know that word but it may be good way to confuse your mates!
Computers are deterministic.
That means that their behaviour must be predictable given the same input and circumstances.
As I have already said you may think computers have a mind of their own and are NOT predictable.
I can assure you they are and there are reasons why they act the way they do. More on that later!

## Slide 11: Activity
Some students like to travel on trains. Not all students like cheese.
Discuss in groups which of the following statements are true based on the statements above.
Students who like cheese do not like to travel on a train
Student who travel by train like eating cheese
Some students who travel by train will like cheese
Students who do not like cheese may still like the train.
Some students who travel by train will like cheese
Students who do not like cheese may still like the train.

## Slide 12: Activity
Open “Logic Gates Activities” Folder
Open “1 - Understanding logic”
Complete all activities

## Slide 13: Types of Logic Gates
There are three main logic gates.
  NOT:
  AND
  OR

## Slide 14: AND Gate
AND:
  The AND gate outputs 1 only if both inputs are 1.
INPUT A
OUTPUT
INPUT B
INPUT A | INPUT B | OUTPUT
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 15: OR Gate
OR:
  The OR gate outputs 1 if either of the inputs is 1.
INPUT A
OUTPUT
INPUT B
INPUT A | INPUT B | OUTPUT
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 16: NOT Gate
The NOT gate is a converter:
  If 0 is input then it outputs 1;
  If 1 is input then it outputs 0.
INPUT
OUTPUT
INPUT | OUTPUT
0 | 1
1 | 0

## Slide 17: Activity
For all of these questions assume that
A = True (1)
B = False (0)
Write down if the result will be true or false.
A AND B
NOT B
NOT A
A OR B
NOT (A AND B)
NOT (A AND B) OR (A AND B)
(A AND B) OR (A OR B)
NOT (A OR B) AND (A OR B)

## Slide 18: Starter
Log on and complete the following in your book
For all of these questions assume that
A = False (0)
B = True (1)
Write down if the result will be true or false.
Draw the Gate in http://logic.ly/demo/ and Truth Table in power point or word document
A OR B
NOT A
NOT B
A AND B
NOT (A OR B)
NOT (A AND B) OR (A OR B)
(A AND B) AND (A OR B)
X = NOT (A OR B) OR (A OR B)

## Slide 19: Logic gates
Now that we have an idea of truth and understand this on / off / 1 / 0 malarkey we can move onto logic gates.
You will need to be able to read them, append to them and create them. You will also be expected to create truth tables from them.
Below are what AND / OR and NOT look like

## Slide 20: Remembering them!
You need to remember these symbols. Let us use some memory techniques to help.
The OR looks a bit like a badge. There is lots of badges to choose from but your only allowed to wear one. So could it be that one OR that one OR that one ....
NOT has a circle at the end which is a bit like a full stop. You are NOT having that, full stop!!!
AND looks a bit like a pac man ghost. Pacman needs to eat power kills AND avoid ghosts.

## Slide 21: Activity
Open “Logic Gates Activities” Folder
Open “2- truth table” and “3- Logic Gate Tasksheet 3”
Complete all activities

## Slide 22: Combining Binary Logic
These logic circuits can be combined to make more complex ones: for example, AND and NOT.
INPUT A
INPUT B
OUTPUT
Output used as next INPUT
INPUT A | INPUT B | OUTPUT
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
INPUT | OUTPUT
0 | 1
0 | 1
0 | 1
1 | 0
OUTPUT A AND B

## Slide 23: Combining Binary Logic
This circuit contains a AND gate and a NOT gate:
The inputs A and B are processed first by the AND gate.
That output is then processed by the NOT gate.
We write this combination as NOT(A AND B).
INPUT A
INPUT B
OUTPUT

## Slide 24: Combining Binary Logic
George Boole, an English mathematician, developed this way of writing down logical expressions (Boolean algebra).
The expression NOT(A OR B) refers to this diagram:
INPUT A
INPUT B
OUTPUT

## Slide 25: Combining Binary Logic Truth Table
We use a table showing all the possible inputs and the resulting outputs to describe what the logic circuit does. This is called a truth table.
For the expression P = NOT(A OR B) the truth table can be derived:
INPUT A | INPUT B | A OR B | P = NOT(A OR B)
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0

## Slide 26: Starter
The diagram below shows three inputs (A, B and C).
In a your revision power point state the equation the diagram below
Create the truth table for the diagram below

## Slide 27: More Than 2 Inputs
It is possible to have more than 2 inputs.
The diagram below shows three inputs (A, B and C).
The equation is Z = (A OR B) AND (NOT C)
A | B | C | Z
1 | 1 | 0 | 1
1 | 0 | 0 | 1
0 | 1 | 0 | 1
0 | 0 | 0 | 0
1 | 1 | 1 | 0
1 | 0 | 1 | 0
0 | 1 | 1 | 0
0 | 0 | 1 | 0
So how did I make this?
Let go through the steps

## Slide 28: Step 1 – Write out all the permutations
The first step is write down all of the possibilities.
As there are now 3 inputs there are extra rows.
A | B | C
1 | 1 | 0
1 | 0 | 0
0 | 1 | 0
0 | 0 | 0
1 | 1 | 1
1 | 0 | 1
0 | 1 | 1
0 | 0 | 1
Every possibility must be written down. As a rule of thumb
1 input = 2 rows
2 inputs = 4 rows
3 inputs = 8 rows
4 inputs = 16 rows..
They double each time!
Tip:
When you add a extra output copy all of the rows and then add 0’s in the new input for the first half and 1’s for the second half.

## Slide 29: Step 2 – Perform the First Logic Gate
Now we create a new column for the first logic gate.
That will help us work out the output of that gate.
This will then be the input to the next!
A | B | C | A OR B
1 | 1 | 0 | 1
1 | 0 | 0 | 1
0 | 1 | 0 | 1
0 | 0 | 0 | 0
1 | 1 | 1 | 1
1 | 0 | 1 | 1
0 | 1 | 1 | 1
0 | 0 | 1 | 0

## Slide 30: Step 3 – Do the Same for the Next Logic Gate
We just add a new column for each logic gate.
Things are starting to take shape!
A | B | C | A OR B | NOT C
1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0

## Slide 31: Step 4 – The Result!
Z = (NOT C) AND (A OR B)
A | B | C | A OR B | NOT C | Z
1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0

## Slide 32: Activity
Write down the equation related to this diagram and then create a truth table.
L
D
K
The key to success here is HOW you do it, not the answer!
A

## Slide 33: Answers: Truth Table
Equation is K = (NOT (L AND D)) AND (NOT A)
Step 1: To create a truth table; we find out all the possibilities for three inputs
  To find out all the possibilities we find out binary representation of 0 – 7 in 3-bit Example
A | D | L
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
= 0
= 1
= 2
= 3
= 4
= 5
= 6
= 7
4 | 2 | 1

## Slide 34: Answers: Truth Table
Equation is K = NOT (L AND D) AND (NOT A)
Step 2: we find out L AND D
Step 3: we find out NOT A
Step 4: we find out the outcome of (L AND D) AND (NOT A)
Step 5: We finally workout K = NOT (L AND D) AND (NOT A)
A | D | L
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
L AND D
0
0
0
1
0
0
0
1
NOT A
1
1
1
1
0
0
0
0
K
1
1
1
0
1
1
1
1
(L AND D) AND (NOT A)
0
0
0
1
0
0
0
0

## Slide 35: Activity
Complete the Logic Gate activity Cards, for each card;
  Create this circuit on http://logic.ly/demo/
  Copy the truth Table and complete it
  Describe how this gate works

## Slide 36: Activity
  Open the “Logic Gates Activities” Folder
  Work through the worksheet
  Start with BinaryLogic_Exercises and BinaryLogic_Assessment
Complete the Logic Gate activity Cards, for each card;
  Create this circuit on http://logic.ly/demo/
  Copy the truth Table and complete it
  Describe how this gate works
And